## Slide 1: Applied Sciences Faculty Management Information Systems
Dr. Yakup BAKIŞ
Notes: Hi everyone! My name is Yakup. I’ll be your instructor for Web Design and Programming. Before we start, I’d like to briefly introduce myself…

## Slide 2: Assignment 2
Chapter 1 Review Questions
SECTION 1.5 (R24, R25)
Chapter 1 Problems Questions
P6, P7, P8, P9, P10, P13, P14, P18, P25, P26, P27, P28, P29, P31,
Run three traceroutes Deliverable:A short 1-page report with:
screenshot of both outputs,
your answers in 5–8 sentences.
Then answer: How many hops for each?
Where do you first see a big increase in RTT?
Do you see any *? What could explain them?
Are there private IP addresses?
What do they suggest about the network path?

## Slide 3: Assignment 1
Submission
          Format: PDF or Word
          Length: 1–2 pages
          Due: Next week before class

## Slide 4: Assignment 1
Chapter 1 Review Questions
SECTION 1.1
R1. What is the difference between a host and an end system? List several different types of end systems. Is a Web server an end system?
SECTION 1.2
R4. List four access technologies. Classify each one as home access, enterprise access, or wide-area wireless access.
R7. What is the transmission rate of Ethernet LANs?
R9. HFC, DSL, and FTTH are all used for residential access. For each of
these access technologies, provide a range of transmission rates and comment on whether the transmission rate is shared or dedicated.
SECTION 1.5
R24. What is an application-layer message? A transport-layer segment? A net work-layer datagram? A link-layer frame?
R25. Which layers in the Internet protocol stack does a router process? Which layers does a link-layer switch process? Which layers does a host process?

## Slide 5
Problem 2: At time N*(L/R) the first packet has reached the destination, the second packet is stored in the last router, the third packet is stored in the next-to-last router, etc. At time N*(L/R) + L/R, the second packet has reached the destination, the third packet is stored in the last router, etc. Continuing with this logic, we see that at time N*(L/R) + (P-1)*(L/R) = (N+P-1)*(L/R) all packets have reached the destination.

## Slide 6
1. There is no difference. Throughout this text, the words “host” and “end system” are used interchangeably. End systems include PCs, workstations, Web servers, mail servers, PDAs, Internet-connected game consoles, etc.
4. 1. Dial-up modem over telephone line: home; 2. DSL over telephone line: home or small office; 3. Cable to HFC: home; 4. 100 Mbps switched Ethernet: enterprise; 5. Wifi (802.11): home and enterprise: 6. 3G and 4G wide-area wireless.
7. Ethernet LANs have transmission rates of 10 Mbps, 100 Mbps, 1 Gbps and 10 Gbps.
9. Dial up modems: up to 56 Kbps, bandwidth is dedicated; ADSL: up to 24 Mbps downstream and 2.5 Mbps upstream, bandwidth is dedicated; HFC, rates up to 42.8 Mbps and upstream rates of up to 30.7 Mbps, bandwidth is shared. FTTH: 2-10Mbps upload; 10-20 Mbps download; bandwidth is not shared.
24. Application-layer message: data which an application wants to send and passed onto the transport layer; transport-layer segment: generated by the transport layer and encapsulates application-layer message with transport layer header; network-layer datagram: encapsulates transport-layer segment with a network-layer header; linklayer frame: encapsulates network-layer datagram with a link-layer header.
25. Routers process network, link and physical layers (layers 1 through 3). (This is a little bit of a white lie, as modern routers sometimes act as firewalls or caching components, and process Transport layer as well.) Link layer switches process link and physical layers (layers 1 through2). Hosts process all five layers.

## Slide 7
P6. This elementary problem begins to explore propagation delay and transmission delay, two central concepts in data networking. Consider two hosts, A and B, connected by a single link of rate R bps. Suppose that the two hosts are separated by m meters, and suppose the propagation speed along the link is s meters/sec. Host A is to send a packet of size L bits to Host B.
a. Express the propagation delay, dprop, in terms of m and s.
b. Determine the transmission time of the packet, dtrans, in terms of L and R.
c. Ignoring processing and queuing delays, obtain an expression for the end-to-end delay.
d. Suppose Host A begins to transmit the packet at time t = 0. At time t = dtrans, where is the last bit of the packet?
e. Suppose dprop is greater than dtrans. At time t = dtrans, where is the first bit of the packet?
f. Suppose dprop is less than dtrans. At time t = dtrans, where is the first bit of the packet?
g. Suppose s = 2.5 # 108, L = 1500 bytes, and R = 10 Mbps. Find the distance m so that dprop equals dtrans.

## Slide 8
Problem 6:
a) dprop = m / s seconds.
b) dtrans = L / R seconds.
c) dend −to−end = (m / s + L / R) seconds.
d) The bit is just leaving Host A.
e) The first bit is in the link and has not reached Host B.
f) The first bit has reached Host B.
g) Want