## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 3 Transport Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: These notes are written by the instructor for students to review after class. This title slide marks the beginning of the week's main topic.
Students should treat this week as a connected story rather than a list of isolated definitions. Focus on what problem each protocol or mechanism is trying to solve and how that idea connects to the slides that follow.

## Slide 2: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.
This slide starts a short sequence and introduces the key idea.

## Slide 3: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: This slide summarizes TCP as a reliable, connection-oriented, byte-stream protocol. Students should connect each listed feature to a concrete need such as ordered delivery, flow control, or connection setup.
The key lesson is that TCP adds structure and state so that applications can exchange data safely over an imperfect network.

## Slide 4: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification
Notes: This slide focuses on header fields. Sequence number, acknowledgement number, receive window, flags, and checksum are the fields that drive most of TCP behavior.
Students should not see the header as a static format only; it is the place where TCP expresses reliability, flow control, and connection management.

## Slide 5: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
Notes: This slide explains how TCP uses byte-oriented numbering and cumulative acknowledgements. The sender and receiver do not merely exchange packets; they track progress inside a continuous byte stream.
Students should read the examples carefully and ask what each side knows at that moment.
This slide starts a short sequence and introduces the key idea.

## Slide 6: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: This slide explains how TCP uses byte-oriented numbering and cumulative acknowledgements. The sender and receiver do not merely exchange packets; they track progress inside a continuous byte stream.
Students should read the examples carefully and ask what each side knows at that moment.
This slide closes the sequence and highlights the takeaway point.

## Slide 7: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT
Notes: This slide discusses RTT estimation and timeout selection. TCP cannot rely on a fixed delay value because network conditions change over time.
Students should understand the reason for smoothing, variation tracking, and adaptive timeout behavior rather than memorizing the formula only.
This slide starts a short sequence and introduces the key idea.

## Slide 8: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: This slide discusses RTT estimation and timeout selection. TCP cannot rely on a fixed delay value because network conditions change over time.
Students should understand the reason for smoothing, variation tracking, and adaptive timeout behavior rather than memorizing the formula only.
This slide continues the example sequence and adds another step.

## Slide 9: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
Notes: This slide discusses RTT estimation and timeout selection. TCP cannot rely on a fixed delay value because network conditions change over time.
Students should understand the reason for smoothing, variation tracking, and adaptive timeout behavior rather than memorizing the formula only.
This slide closes the sequence and highlights the takeaway point.

## Slide 10: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.

## Slide 11: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.

## Slide 12: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide starts a short sequence and introduces the key idea.

## Slide 13: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide closes the sequence and highlights the takeaway point.

## Slide 14: TCP fast retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: This slide explains how TCP uses byte-oriented numbering and cumulative acknowledgements. The sender and receiver do not merely exchange packets; they track progress inside a continuous byte stream.
Students should read the examples carefully and ask what each side knows at that moment.

## Slide 15: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.
This slide continues the example sequence and adds another step.

## Slide 16: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide starts a short sequence and introduces the key idea.

## Slide 17: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide continues the example sequence and adds another step.

## Slide 18: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
from sender
Application removing data from TCP socket buffers
receive window
flow control: # bytes receiver willing to accept
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide continues the example sequence and adds another step.

## Slide 19: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control
from sender
Application removing data from TCP socket buffers
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide continues the example sequence and adds another step.

## Slide 20: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP receiver-side buffering
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide continues the example sequence and adds another step.

## Slide 21: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
flow control: # bytes receiver willing to accept
receive window
TCP segment format
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.
This slide closes the sequence and highlights the takeaway point.

## Slide 22: TCP connection management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: This slide explains retransmission behavior. Timeout, cumulative ACKs, duplicate ACKs, and fast retransmit all exist because the sender must recover from uncertainty.
Students should trace each scenario step by step and identify why the sender retransmits at that exact moment.

## Slide 23: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.

## Slide 24: 2-way handshake scenarios
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.
This slide starts a short sequence and introduces the key idea.

## Slide 25: 2-way handshake scenarios
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.
This slide continues the example sequence and adds another step.

## Slide 26: 2-way handshake scenarios
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
Problem: dup data
accepted!
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.
This slide closes the sequence and highlights the takeaway point.

## Slide 27: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
LISTEN
Server state
LISTEN
clientSocket = socket(AF_INET, SOCK_STREAM)
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
connectionSocket, addr = serverSocket.accept()
clientSocket.connect((serverName,serverPort))
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.

## Slide 28: A human 3-way handshake protocol
1. On belay?
2. Belay on.
3. Climbing.
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.

## Slide 29: Closing a TCP connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
Notes: This slide covers connection management. TCP must establish shared state before data transfer and close the connection cleanly afterward.
Students should understand why two-way handshake is insufficient in a real network and why three-way handshake is the standard solution.

## Slide 30: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.
This slide closes the sequence and highlights the takeaway point.