## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 4 Network Layer:
Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: These notes are written by the instructor for students to review after class. This title slide marks the beginning of the week's main topic.
Students should treat this week as a connected story rather than a list of isolated definitions. Focus on what problem each protocol or mechanism is trying to solve and how that idea connects to the slides that follow.

## Slide 2: Network layer: our goals
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  addressing
  generalized forwarding
  Internet architecture
instantiation, implementation in the Internet
  IP protocol
  NAT, middleboxes
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.

## Slide 3: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.
This slide starts a short sequence and introduces the key idea.

## Slide 4: Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 5: Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 6: Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 7: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 8: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 9: Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 10: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.
This slide starts a short sequence and introduces the key idea.

## Slide 11: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.
This slide closes the sequence and highlights the takeaway point.

## Slide 12: Reflections on best-effort service:
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 13: Network layer: “data plane” roadmap
Network layer: overview
  data plane
  control plane
What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
Middleboxes
Notes: This roadmap slide is a guide for the rest of the lecture. Students should use it to keep the chapter organized and to see where the current slide fits in the larger flow.
When reviewing, it is useful to group the material into blocks rather than memorizing slide by slide.
This slide closes the sequence and highlights the takeaway point.

## Slide 14: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
Notes: This slide explains the network-layer service model or the difference between forwarding and routing. Students should distinguish local router action from network-wide path selection.
The Internet's best-effort model is important because later protocols and applications are designed on top of that limited but scalable service.

## Slide 15: Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
Notes: This slide explains what happens inside a router. Input ports, switching fabric, output ports, and control logic together determine forwarding performance.
Students should think in terms of packet movement through components, not only in terms of abstract diagrams.
This slide starts a short sequence and introduces the key idea.

## Slide 16: Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
Notes: This slide explains what happens inside a router. Input ports, switching fabric, output ports, and control logic together determine forwarding performance.
Students should think in terms of packet movement through components, not only in terms of abstract diagrams.
This slide closes the sequence and highlights the takeaway point.

## Slide 17: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3
Notes: This slide continues the week's main topic. Students should identify the central problem, the mechanism shown on the slide, and the practical reason the protocol or device behaves that way.
A good review strategy is to ask what this slide adds compared with the previous one and how it supports the next step in the chapter.

## Slide 18: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001
Notes: This slide explains longest-prefix matching. When more than one forwarding entry matches a destination, the most specific prefix must be selected.
Students should practice these examples because they are central to destination-based forwarding questions.
This slide starts a short sequence and introduces the key idea.

## Slide 19: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Notes: This slide explains longest-prefix matching. When more than one forwarding entry matches a destination, the most specific prefix must be selected.
Students should practice these examples because they are central to destination-based forwarding questions.
This slide continues the example sequence and adds another step.

## Slide 20: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Notes: This slide explains longest-prefix matching. When more than one forwarding entry matches a destination, the most specific prefix must be selected.
Students should practice these examples because they are central to destination-based forwarding questions.
This slide continues the example sequence and adds another step.

## Slide 21: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!
Notes: This slide explains longest-prefix matching. When more than one forwarding entry matches a destination, the most specific prefix must be selected.
Students should practice these examples because they are central to destination-based forwarding questions.
This slide closes the sequence and highlights the takeaway point.

## Slide 22: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM
Notes: This slide explains longest-prefix matching. When more than one forwarding entry matches a destination, the most specific prefix must be selected.
Students should practice these examples because they are central to destination-based forwarding questions.

## Slide 23: Switching fabrics
transfer packet from input link to appropriate output link
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 24: Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 25: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 26: Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 27: Switching via interconnection network
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 28: Switching via interconnection network
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 29: Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 30: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
This is a really important slide
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.
This slide starts a short sequence and introduces the key idea.

## Slide 31: Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.
This slide closes the sequence and highlights the takeaway point.

## Slide 32: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gbps link: 2.5 Gbit buffer
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for realtime apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough (busy) but no fuller”
RTT C
.
N
more recent recommendation: with N flows, buffering equal to
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.

## Slide 33: Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
Notes: This slide is about switching fabrics or internal transfer inside routers. The central question is whether the internal architecture can keep up with external line rates.
Students should compare memory-based, bus-based, and interconnection-network approaches in terms of speed and scalability.

## Slide 34: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.

## Slide 35: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.

## Slide 36: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.

## Slide 37: Scheduling policies: weighted fair queueing
Weighted Fair Queuing (WFQ):
generalized Round Robin
classify
arrivals
departures
link
R
w1
w2
w3
wi
Sjwj
minimum bandwidth guarantee (per-traffic-class)
each class, i, has weight, wi, and gets weighted amount of service in each cycle:
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.

## Slide 38: Sidebar: Network Neutrality
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition
  enforced legal rules and policies
Different countries have different “takes” on network neutrality
Notes: This slide discusses queueing, buffering, or scheduling. Delays and losses appear whenever packets arrive faster than the router can switch or transmit them.
Students should pay attention to HOL blocking, overflow, drop policies, and scheduling fairness because these determine real forwarding quality.
This slide starts a short sequence and introduces the key idea.

## Slide 39: Sidebar: Network Neutrality
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”
no paid prioritization. … “shall not engage in paid prioritization”
Notes: This slide connects technical packet treatment to broader fairness and policy questions. Scheduling and prioritization are not only engineering choices; they can affect openness and neutrality.
Students should see why network-layer mechanisms sometimes have social and regulatory consequences.
This slide closes the sequence and highlights the takeaway point.

## Slide 40: ISP: telecommunications or information service?
US Telecommunication Act of 1934 and 1996:
  Title II: imposes “common carrier duties” on telecommunications services: reasonable rates, non-discrimination and requires regulation
  Title I: applies to information services:
    no common carrier duties (not regulated)
    but grants FCC authority “… as may be necessary in the execution of its functions”4
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!
Notes: This slide connects technical packet treatment to broader fairness and policy questions. Scheduling and prioritization are not only engineering choices; they can affect openness and neutrality.
Students should see why network-layer mechanisms sometimes have social and regulatory consequences.